What a Drag!

Accommodating Assumptions

Michael Brune and Sandy Powell

Teacher’s Guide

Lesson Overview and Content Focus

Engineering problems rarely have one right answer. Models and simulations are frequently used to determine the best available solution. However, not all simulations are created equal. For example, simulations of the flight of water rockets differ in the results given based upon assumptions made by the simulation creator.

This lesson gives students an introduction to the use of simulations to model the flight of water rockets and then uses the Euler Method to make similar calculations. Different assumptions required to simulate flight involving drag are introduced and students learn the importance of running multiple instances of a simulation (a Monte Carlo Simulation).

The culminating activity is an engineering design challenge where students use a model and simulations to design a water rocket to land a given distance from the launch pad.

Grade Level and Student Prerequisites

Intended for use in high school Calculus or Physics courses

Student Prerequisites

Before beginning this lesson students should be able to:

- Use basic ballistics equations

- Correctly complete unit conversions

Learning Objectives

The student will be able to:

- Solve Ballistics Equations involving drag using the Euler method of integration

- Vary default values to create a Monte Carlo Graph using a simulation.

- Use the Engineering Process to solve a complex problem.

- Compare results of simulations with experimental testing.

- Communicate results.

Materials and Resources

Handouts

Student Preparation Webquest Worksheet

Calculating Position with Drag Worksheet

Monte Carlo Graph

Request for Proposals

Proposal Presentation Rubric/Scoresheet

Rocket Stability Handout

Internet

Websites:

- Beginners Guide to Aeronautics: http://www.grc.nasa.gov/WWW/K-12/airplane/

Trajectory Simulations:

- PhET: http://phet.colorado.edu/en/simulation/projectile-motion (Select “Run Now”)

- HyperPhysics: http://hyperphysics.phy-astr.gsu.edu/hbase/traj.html (scroll down to “Where will it land?”)

Water Rocket Simulations:

- Science Bits: http://www.sciencebits.com/RocketCalculator?fromForm=yes

- NASA: http://microgravity.grc.nasa.gov/education/rocket/BottleRocket/sim.htm

- Brigham Young University: http://www.et.byu.edu/~wheeler/benchtop/sim.php

- Water-Rockets.com: http://www.water-rockets.com/article.pl?4

Equipment

Water Rocket Launcher (building instructions also available from NASA at http://www.nasa.gov/audience/foreducators/topnav/materials/listbytype/Water_Rocket_Launcher_Directions.html)

Air compressor

Dice (2 per group) or other random number generator

Penny (1 per group)

Timer

Measuring tape (50 or 100 ft)

Safety Glasses

2 Liter plastic bottles

Water rocket construction materials

Transparent Graph (1 per pair – print Monte Carlo Graph handout on overhead transparency pages)

Overhead Marker (1 per pair)

Overhead Projector

Presentation Materials (Posters, markers, rulers, overhead, computers, projector)

Supplemental Readings or Websites

- Water Rocket Construction Instructions (see below or http://www.nasa.gov/audience/foreducators/topnav/materials/listbytype/Water_Rocket_Construction.html)

Other

- Monte Carlo Values Excel Spreadsheet

Time Required (7 days - based on 45 minute class periods)

Student Preparation Webquest Worksheet (1 day – in computer lab)

Calculating Position with Drag Worksheet (1 day in classroom)

Monte Carlo Simulation Activity (1 day in computer lab)

Engineering Project (2 days in computer lab and classroom)

Launch Day (1 day outside)

Presentations (1 day in classroom)

Background

What is the Orion MPCV?

The Orion Multi-Purpose Crew Vehicle will be the newest addition to NASA’s manned space flight vehicles.  The goal of the Orion MPCV is to allow astronauts to travel into space to possibly land on the moon and nearby asteroids.  The Orion MPCV crew module is considerably larger than the Apollo crew module and will allow for more astronauts as well as a greater amount of payload to be taken to and from space bodies.

What is the LAS?

LAS stands for launch abort system.  For the Orion Multi-Purpose Crew Vehicle NASA chose to create a safety system that would allow astronauts to abort the mission and return safely to earth.  This can happen in different ways.  The mission can be aborted while the rocket is still on the ground (pad abort), or it can be aborted after launch before the rocket is in a zero gravity situation.  The LAS works by firing rockets on the boom above the crew module, thereby accelerating the crew module away from the rest of the vehicle.  When this occurs astronauts will encounter a force greater than twelve times the force of gravity.  After separation the LAS module will begin firing small boosters near the nose of the rocket to guide the crew module through a rotation orienting the module for chute deployment.  The LAS will then disconnect from the crew module and the crew module will go through a chute deployment routine allowing it to slow its trajectory before landing in the ocean.

How are Water Rockets related to the LAS?

The LAS has a very short thrust phase that only serves to separate the crew module from the rest of the rocket body.  Though this thrust phase is very brief, it creates a great amount of propulsion.  Similarly, a water bottle rocket only has thrust until all the water in the bottle is expelled.  In most cases, this occurs within 0.03 seconds of launch.  In this sense, the launch phase of a water bottle rocket closely matches that of the LAS. When a pad abort takes place, the LAS must use the short thrust phase to achieve a height great enough to allow the crew module time to safely cycle through its chute deployment routine.  If the launch cycle takes too long to reach this height, however, then the guidance boosters will exhaust their limited fuel supply, leaving the crew module rotations up to chance.  It also must achieve a distance great enough to allow the LAS to land in the ocean.  The bottle rocket problem models these engineering requirements of the LAS by requiring the bottle rockets to maintain a loft time that falls within a specific range as well as a distance that falls within a specific range.

Why are we concerned about assumptions?

As NASA engineers address the complex formulas necessary to solve the problems they face, they have to make assumptions about the data that they are using.  These assumptions can take many forms.  An engineer may assume that the atmospheric pressure on a certain launch day will be the same as what it was on the same day a year earlier, or they may assume that a rocket will remain nose forward throughout its entire flight path, or perhaps they assume that the capsule carrying the rover to Mars will arrive with no damage to its hull and be able to maintain a predicted landing trajectory.  These assumptions may seem innocent, but if the assumption is not correct then error will be introduced into the engineering problem.  Simple changes to the assumed data can add up which can create undesirable outcomes.  To anticipate any outcomes that may be due to assumptions NASA engineers will conduct a simulation called a Monte Carlo.

A Monte Carlo simulation takes into account likely data for a specific situation and generates thousands of possible outcomes in the form of data points on a grid.  It does this by varying the individual data elements the engineer believes could change while combining many of the ways these individual data elements could mix together to create differing results.  These results are then plotted and illustrate how the actual event could vary from what was originally modeled.

One example is a Monte Carlo simulation that was completed for the rovers landing on Mars.  Before either rover was sent, NASA engineers decided they wanted the rover to land within a crater to gather samples.  After setting the base values of the model to land in the center of the crater, engineers created a Monte Carlo based on their data that displayed possible landing deviations due to changes in the expected condition of the rocket.  The Monte Carlo illustrated that there was a very small probability that the rover would land outside of its landing zone as only a few points out of thousands and thousands fell outside of the safe landing zone.

These simulations allow researchers to predict what will happen if the systems they design don’t work as expected and ensure that a project such as the Mars rover doesn’t fail after millions of dollars have been spent to get the rover to Mars.

Procedure

Day 1: Introduction – in Computer Lab

Preparation: Make a copy of Requisite Skills WebQuest Worksheet for each student.

- Have students watch the introductory videos (3 minutes).

- Introduce the relationship between water bottle rockets and the Launch Abort System, especially during a pad abort (5 minutes).

- Give each student a copy of the Requisite Skills WebQuest Worksheet and allow class time for completion (30 minutes).

- Discuss in class what students think causes the differences between the simulations that include drag. Introduce and discuss the concept of assumptions when building an environmental model. Suggest students look at the underlying assumptions of the models found on websites including descriptions of the equations used (7 minutes).

Day 2: Euler’s Method – in Classroom

Preparation: Make a copy of Calculating Position with Drag for each student.

- Show students an example of a basic trajectory using a ballistic model.  Relate to the PhET and HyperPhysics simulations from the Day 1worksheet. Discuss whether such a trajectory is realistic outside of the classroom (3 minutes).

- Introduce the concept of drag and have students sketch what they believe the path of an object may look like if drag were included. Encourage them to think about the water rocket simulations from the Day 1worksheet (3 minutes).

- Handout the Calculating Position with Drag worksheet and discuss with students the initial conditions. Have students fill in the initial conditions as they are discussed (8 minutes).

- Consider with the class how velocity is affected by drag, and the fact that as time passes the angle of attack and the velocity will continually change in response to the drag force (changing as time changes).  Allow the class to consider what approach might be necessary to calculate the effect of such a force (8 minutes).

- Begin working together on the Euler Drag worksheet, fill in the first few rows together and plot the distance downrange (x) vs. the height (y) as a class until all students understand how to continue the process as time passes (15 minutes).

- Briefly discuss how the model could be made more accurate (2 minutes).

- Instruct students to continue working the problem until the rocket hits the ground and to return the next day with the finished graph (6 minutes).

Day 3: Monte Carlo Simulation – in Computer Lab

Preparation: Make a transparent copy of Monte Carlo Graph for each pair of students. Make a copy of Monte Carlo Graph Simulation Instructions for each pair of students.

- Break students into pairs.

- Open the excel spreadsheet WhatADrag_MonteCarlo.xls.

- Distribute transparent copy of Monte Carlo Graph, Simulation Instructions handout, overhead marker, two dice (or other random number generating device), and a coin to each group.

- Introduction to a Monte Carlo Simulation (8 minutes).

  - Have students plot on their graphs the distance downrange vs. time of flight (yellow highlighted cells) for the default conditions. This is called the nominal case.

  - Explain that engineers use a Monte Carlo Simulation to see what the likely outcomes are for a given situation. Since the default conditions may contain errors and to accommodate the assumptions made in designing a simulation, a series of iterations of the simulation are run with small changes made to the initial conditions.

Engineers select a range of values (usually 10% – 20% change above and below the nominal conditions) for each initial condition. The engineers then program the simulation to run hundreds of times while changing each of the conditions by a different random value for each run.

Rather than have the computer change the values randomly, students will use dice (or other random number generator) and a penny to determine the amount of change for each condition. They will then graph their results, and repeat the process as many times as possible in the given time.

  - Walk the students through finding one data point for the simulation with the students using the Monte Carlo Graph Simulation Instructions.

- Students should repeat the process to find and plot new data points to ensure that their Monte Carlo graph contains many points. (25 minutes)

- Collect the student graphs about ten minutes before the end of the period.  Overlay the transparent graphs on an overhead projector or with a backlit document camera to display all the resulting data points in one graph.  Discuss with the students that even though we believe our assumptions are valid, even small changes in those assumptions result in different data.  To accommodate the range of assumption errors engineers will create a Monte Carlo Graph.  Engineers and scientists will then base their expected outcomes on the results of the Monte Carlo rather than depending exclusively on the results of a single simulation or computation (10 minutes).

Days 4-5: Project – in Computer Lab and Classroom

Preparation: Make a paper copy of Monte Carlo Graph for each team of students.

- Break students into groups with an ideal size of 3 members.

- Introduce the project by handing out and discussing the NASA Request for Proposals document. (5 minutes)

- Refer to the Water Rocket Construction at: http://www.nasa.gov/pdf/153406main_Rockets_Water_Rocket_Construction.pdf
or link to it from the website: http://www.nasa.gov/audience/foreducators/topnav/materials/listbytype/Rockets.html

- Provide material to the student groups and have them begin constructing their water rockets.  Distribute the Rocket Stability Determination handout to remind students to consider center of mass, center of pressure, and stability of their rocket.

- Allow students class time to design and build their rocket.

- Make certain that the computer lab is available as well as graph paper for students to conduct Monte Carlo simulations for the rockets they construct.

Break: 2 days for students to work outside of class.  If this is not a weekend, then other in-class   
 	material should be presented.

Day 6: Launch - Outside

Preparation: Select Launch Site. Optional: Mark distance minimum and maximum locations using rope, cones, or other materials.

- With air compressor, launch pad, and water available take all groups outside for the launch activity.

- Ensure that graph paper, pencils, 200ft tape measure, and a timer are available for students to plot their outcomes.

- Launch area should be marked for easy identification of acceptable downrange distances.

- Allow each group to launch their rocket three to five times (depending on time) and collect distance and time of flight data.

Break: 2 days for students to work outside of class. If this is not over a weekend then other in-
 	class material should be presented.

Day 7: Presentations

- Distribute Proposal Presentation Reviewer Scoresheet to all students in class so that they can score their peers as well as their own team.

- Allow teams to present their data, explain their Monte Carlo output, the launch conditions they selected and to justify the decisions they made throughout the process.

- As each team finishes their presentation allow 1-2 minutes for their peers to assess their methodology and then move on to the next presentation.

- Congratulate students on improving their engineering expertise.  If desired, a reward may be given to the team with the best approach to the problem as judged by the instructor and, to a smaller extent, the grading of their peers.

Students Assessment(s)

Student Preparation Webquest Worksheet

Calculating Position with Drag Worksheet

Monte Carlo Graph

Proposal Presentation Scoresheet

Alignment with National and State Standards

Common Core Standards

English Language Arts 6-12 (http://www.corestandards.org/assets/CCSSI_ELA%20Standards.pdf)

Reading Standards for Literacy in Science and Technical Subjects 
6-12

Key Ideas and Details

R-ST3. Follow precisely a complex multistep procedure when carrying out experiments, taking measurements, or performing technical tasks; analyze the specific results based on explanations in the text.

Integration of Knowledge and Ideas

R-ST7. Integrate and evaluate multiple sources of information presented in diverse formats and media (e.g., quantitative data, video, multimedia) in order to address a question or solve a problem

R-ST8. Evaluate the hypotheses, data, analysis, and conclusions in a science or technical text, verifying the data when possible and corroborating or challenging conclusions with other sources of information

R-ST9. Synthesize information from a range of sources (e.g., texts, experiments, simulations) into a coherent understanding of a process, phenomenon, or concept, resolving conflicting information when possible

Mathematics 6-12

(http://www.corestandards.org/assets/CCSSI_Math%20Standards.pdf)

S-ID6: Represent data on two quantitative variables on a scatter plot, and

describe how the variables are related.

S-IC1: Understand statistics as a process for making inferences about

population parameters based on a random sample from that population.

S-IC5: Use data from a randomized experiment to compare two treatments;

use simulations to decide if differences between parameters are significant.

N-Q1: Use units as a way to understand problems and to guide the solution

of multi-step problems; choose and interpret units consistently in

formulas; choose and interpret the scale and the origin in graphs and

data displays.

N-Q2: Define appropriate quantities for the purpose of descriptive modeling.

N-Q33: Choose a level of accuracy appropriate to limitations on measurement

when reporting quantities.

N-VM3: Solve problems involving velocity and other quantities that can be represented by vectors.

A-SSE1b: Interpret complicated expressions by viewing one or more of their

parts as a single entity. For example, interpret P(1+r)n as the product

of P and a factor not depending on P.

F-BF1a: Determine an explicit expression, a recursive process, or steps for

calculation from a context.

F-LE1b: Recognize situations in which one quantity changes at a constant

rate per unit interval relative to another.

F-TF7: Use inverse functions to solve trigonometric equations that arise

in modeling contexts; evaluate the solutions using technology, and

interpret them in terms of the context.

Science

National Science Education Standards (Grades 9-12)

(http://www.nap.edu/openbook.php?record_id=4962)

Content Standard A: Science as Inquiry

Abilities necessary to do scientific inquiry

- Identify questions and concepts that guide scientific investigations.

- Design and conduct scientific investigations.

- Use technology and mathematics to improve investigations and communications.

- Formulate and revise scientific explanations and models using logic and evidence.

- Recognize and analyze alternative explanations and models.

- Communicate and defend a scientific argument.

Understandings about scientific inquiry

Content Standard B: Physical Science

Motions and forces

Content Standard E: Science and Technology

Abilities of Technological Design

- Identify a problem or design an opportunity.

- Propose designs and choose between alternative solutions.

- Implement a proposed solution.

- Evaluate the solution and its consequences.

- Communicate the problem, process, and solution.

Understandings about science and technology

CONTENT STANDARD F: Science in Personal and Social Perspectives

Science and technology in local, national, and global challenges

Content Standard G: History and Nature of Science

Science as a human endeavor

Nature of scientific knowledge

Idaho State Science Standards (Grades 9-10)
Note: No State Physics Standards currently exist

STANDARD 1: Nature of Science

Goal 1.2: Understand Concepts and Processes of Evidence, Models, and Explanations

Goal 1.6: Understand Scientific Inquiry and Develop Critical Thinking Skills

Goal 1.8: Understand Technical Communication

STANDARD 2: Physical Science

Goal 2.2 Understand the Concepts of Motion and Forces

STANDARD 5: Personal and Social Perspectives; Technology

Goal 5.2: Understand the Relationship between Science and Technology

Mathematics

NCTM Standards

http://www.nctm.org/standards/content.aspx?id=3856

Number and Operation:

Compute Fluently:

- Develop fluency in operations with real numbers, vectors, and matrices, using mental computation or paper-and-pencil calculations for simple cases and technology for more-complicated cases.

- Judge the reasonableness of numerical computations and their results.

Algebra:

Use mathematical Models:

- Use symbolic expressions, including iterative and recursive forms, to represent relationships arising from various contexts.

- Draw reasonable conclusions about a situation being modeled.

Geometry:

Analyze characteristics and properties of two- and three-dimensional geometric shapes and develop mathematical arguments about geometric relationships

- Use trigonometric relationships to determine lengths and angle measures.

Use visualization, spatial reasoning, and geometric modeling to solve problems

- Visualize three-dimensional objects and spaces from different perspectives and analyze their cross sections.

Measurement:

Understand measurable attributes of objects and the units, systems, and processes of measurement.

- Make decisions about units and scales that are appropriate for problem situations involving measurement.

Apply appropriate techniques, tools, and formulas to determine measurements

- Analyze precision, accuracy, and approximate error in measurement situations.

- Apply informal concepts of successive approximation, upper and lower bounds, and limit in measurement situations.

- Use unit analysis to check measurement computations.

Data Analysis and Probability:

Formulate questions that can be addressed with data and collect, organize, and display relevant data to answer them.

- Understand the differences among various kinds of studies and which types of inferences can legitimately be drawn from each.

- Know the characteristics of well-designed studies, including the role of randomization in surveys and experiments.

Problem Solving:

- Build new mathematical knowledge through problem solving.

- Solve problems that arise in mathematics and in other contexts.

- Apply and adapt a variety of appropriate strategies to solve problems.

- Monitor and reflect on the process of mathematical problem solving.

Communication:

- Organize and consolidate their mathematical thinking through communication.

- Communicate their mathematical thinking coherently and clearly to peers, teachers, and others.

- Analyze and evaluate the mathematical thinking and strategies of others.

- Use the language of mathematics to express mathematical ideas precisely.

Connections:

- Recognize and use connections among mathematical ideas.

- Understand how mathematical ideas interconnect and build on one another to produce a coherent whole.

Representation:

- Create and use representations to organize, record, and communicate mathematical ideas.

- Select, apply, and translate among mathematical representations to solve problems.

- Use representations to model and interpret physical, social, and mathematical phenomena.

Calculus Concepts (Based on Idaho Calculus Standards)

http://www.sde.idaho.gov/site/content_standards/math_standards_docs/course/Final%20AP%20Calculus%20August%2021%202008.pdf

II: Derivatives: Application of derivatives.

III: Integrals: Application of integrals
III: Integrals: Numeric approximations to definite integrals

Technology (http://www.iste.org/Content/NavigationMenu/NETS/ForStudents/2007Standards/NETS_for_Students_2007.htm)

1. Creativity and Innovation

Students demonstrate creative thinking, construct knowledge, and develop innovative products and processes using technology.

2. Communication and Collaboration

Students use digital media and environments to communicate and work collaboratively, including at a distance, to support individual learning and contribute to the learning of others.

3. Research and Information Fluency

Students apply digital tools to gather, evaluate, and use information.

4. Critical Thinking, Problem Solving, and Decision Making

Students use critical thinking skills to plan and conduct research, manage projects, solve problems, and make informed decisions using appropriate digital tools and resources.

6. Technology Operations and Concepts

Students demonstrate a sound understanding of technology concepts, systems, and operations.

What a Drag! Accommodating Assumptions

Student/Teacher Resource Pages/Data Collection Pages

- Water Rocket Construction (also available in NASA’s Rockets Educators Guide)

- Water Rocket Launcher (also available in NASA’s Rockets Educators Guide)

- Requisite Skills Webquest Worksheet

- Calculating Position with Drag Worksheet

- Calculating Position with Drag Worksheet Educator’s Supplement

- Monte Carlo Graph and Instructions

- Proposal Presentation Scoresheet

- Proposal Presentation Reviewer Scoresheet

- Rocket Stability (also available in NASA’s Rockets Educators Guide)

Note:

Excel Spreadsheet used to create the Monte Carlo Graph is a separate file: WhatADrag_MonteCarlo.xls.

- What a Drag! Accommodating Assumptions

Requisite Skills Webquest Worksheet

Basics of Water Rocket Design

Having a stable water rocket requires knowing where the center of pressure and center of gravity are for the rocket. Use the webpage Determining Center of Pressure (http://microgravity.grc.nasa.gov/education/rocket/rktcp.html) to answer the next questions.

- What is the projected area of a rocket?

- How can the projected area be used to mechanically determine the center of pressure?

Use the Determining Center of Gravity (http://microgravity.grc.nasa.gov/education/rocket/rktcg.html) webpage to answer the next question.

- How can the center of gravity of a model be found mechanically?

The Rocket Stability webpage (http://microgravity.grc.nasa.gov/education/rocket/rktstab.html) will help you fill in the blanks below correctly.

- To make a stable rocket the center of _______________ (pressure/mass) should be above or in front of the center of _______________ (pressure/mass).

- Describe how to perform the string test to check a model rocket’s stability.

Use the What is Drag webpage (http://www.grc.nasa.gov/WWW/k-12/airplane/drag1.html) to answer these questions.

- What does drag oppose?

- What two things must be present for drag to occur?

Ballistics Equations Simulations

Complete the following data table to compare two simulations that use traditional ballistics equations.

- PhET: http://phet.colorado.edu/en/simulation/projectile-motion (Select “Run Now”)

- HyperPhysics: http://hyperphysics.phy-astr.gsu.edu/hbase/traj.html (scroll down to “Where will it land?”)

|  | PhET | HyperPhysics |
| --- | --- | --- |
| Angle | 65 | 65 |
| Initial Speed | 50 m/s | 50 m/s |
| Mass | 0.2 kg | N/A |
| Diameter | 0.1 m | N/A |
| Height/y |  | -1.2 m |
| Range/x2 |  |  |
| Time/t2 |  |  |

Give two reasons why most high school math and physics problems involving a falling object or a projectile ignore air resistance.

Water Rocket Simulations

Complete the following table with a partner to compare several water rocket simulations involving drag. Convert units as needed – if a value is not given use the simulation default value. Not all values are used in every simulation. Use N/A to indicate a value not used in the simulation.

- Science Bits: http://www.sciencebits.com/RocketCalculator?fromForm=yes

- NASA: http://microgravity.grc.nasa.gov/education/rocket/BottleRocket/sim.htm (Use both Rocket Modeler II and 3D WaterRocketSim prototype Simulator)

- Brigham Young University: http://www.et.byu.edu/~wheeler/benchtop/sim.php

- Water-Rockets.com: http://www.water-rockets.com/article.pl?4

|  | Default Values | Science Bits | NASA II | NASA III | BYU | Water-Rockets |
| --- | --- | --- | --- | --- | --- | --- |
| Empty Rocket Mass | 0.1 kg |  |  |  |  |  |
| Diameter | 0.1 m |  |  |  |  |  |
| Bottle Volume | 2 L |  |  |  |  |  |
| Initial Pressure | 50 psi |  |  |  |  |  |
| Drag Coefficient | 0.31 |  |  |  |  |  |
| Simulation Time Step | 0.001 s |  |  |  |  |  |
| Bottle Diameter | 11.2 cm |  |  |  |  |  |
| Nozzle Diameter | 2.16 cm |  |  |  |  |  |
| Launch Angle | 65o |  |  |  |  |  |
| Nose Cone Shape | None |  |  |  |  |  |
| Payload | None |  |  |  |  |  |
| Fairing | None |  |  |  |  |  |
| Number of fins | 3 |  |  |  |  |  |
| Shape of fins | Trapezoidal |  |  |  |  |  |
| Fin Length | 10 cm |  |  |  |  |  |
| Fin Width | 10 cm |  |  |  |  |  |
| Water Volume | 300 mL |  |  |  |  |  |
| Altitude | 720 m |  |  |  |  |  |
| Launch Rail Length | 1 m |  |  |  |  |  |
| Temperature | 25 oC |  |  |  |  |  |
| Launch Tube Length | 2 cm |  |  |  |  |  |
| Launch Tube Diameter | 2.15 cm |  |  |  |  |  |
| Maximum Speed |  |  |  |  |  |  |
| Maximum Height |  |  |  |  |  |  |
| Range |  |  |  |  |  |  |
| Time |  |  |  |  |  |  |

| Time | Horizontal Velocity (Vx) | Vertical Velocity (Vy) | Velocity (V) |  | Horizontal Position (x) | Vertical Position (y) |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.0 |  |  |  |  |  |  |  |  |
| 0.2 |  |  |  |  |  |  |  |  |
| 0.4 |  |  |  |  |  |  |  |  |
| 0.6 |  |  |  |  |  |  |  |  |
| 0.8 |  |  |  |  |  |  |  |  |
| 1.0 |  |  |  |  |  |  |  |  |
| 1.2 |  |  |  |  |  |  |  |  |
| 1.4 |  |  |  |  |  |  |  |  |
| 1.6 |  |  |  |  |  |  |  |  |
| 1.8 |  |  |  |  |  |  |  |  |
| 2.0 |  |  |  |  |  |  |  |  |
| 2.2 |  |  |  |  |  |  |  |  |
| 2.4 |  |  |  |  |  |  |  |  |
| 2.6 |  |  |  |  |  |  |  |  |
| 2.8 |  |  |  |  |  |  |  |  |
| 3.0 |  |  |  |  |  |  |  |  |
| 3.2 |  |  |  |  |  |  |  |  |
| 3.4 |  |  |  |  |  |  |  |  |
| 3.6 |  |  |  |  |  |  |  |  |
| 3.8 |  |  |  |  |  |  |  |  |
| Time | Horizontal Velocity (Vx) | Vertical Velocity (Vy) | Velocity (V) |  | Horizontal Position (x) | Vertical Position (y) |  |  |
| 4.0 |  |  |  |  |  |  |  |  |
| 4.2 |  |  |  |  |  |  |  |  |
| 4.4 |  |  |  |  |  |  |  |  |
| 4.6 |  |  |  |  |  |  |  |  |
| 4.8 |  |  |  |  |  |  |  |  |
| 5.0 |  |  |  |  |  |  |  |  |
| 5.2 |  |  |  |  |  |  |  |  |
| 5.4 |  |  |  |  |  |  |  |  |
| 5.6 |  |  |  |  |  |  |  |  |
| 5.8 |  |  |  |  |  |  |  |  |
| 6.0 |  |  |  |  |  |  |  |  |
| 6.2 |  |  |  |  |  |  |  |  |
| 6.4 |  |  |  |  |  |  |  |  |
| 6.6 |  |  |  |  |  |  |  |  |
| 6.8 |  |  |  |  |  |  |  |  |
| 7.0 |  |  |  |  |  |  |  |  |
| 7.2 |  |  |  |  |  |  |  |  |
| 7.4 |  |  |  |  |  |  |  |  |
| 7.6 |  |  |  |  |  |  |  |  |
| 7.8 |  |  |  |  |  |  |  |  |

What a Drag! Accommodating Assumptions

Calculating Position with Drag

Drag =

Acceleration along the x-axis:

Acceleration along the y-axis:

Atmospheric density = ___________________ slugs/ft3

V=Velocity = _________________ ft/sec

Angle of attack = __________________ degrees

Drag coefficient = ___________________

S = Cross sectional area = ____________________ ft2

W = Weight of object = ___________________ lbs

g = Gravitational constant = __________________ ft/sec2

m = Mass of object = __________________ slugs

As the object moves through the air the angle of attack and the velocity will change due to drag and gravity.  This makes it impossible to predict the outcome based solely on the input data.  Instead changes in angle and velocity must be considered in very small segments of time.

Though we are given an initial velocity, we will need to understand the horizontal and vertical components of that velocity as they relate to the angle of attack ().

What a Drag! Accommodating Assumptions

Calculating Position with Drag Educators Supplement

The “Calculating Position with Drag” worksheet is given in 3 pages and should be printed back to back.  The third page on the student copy is actually the first page.  It contains the initial conditions and is easy to separate from the table data after printing.

The first step to completing the worksheet is filling in the initial conditions.  Below is each condition with data entered (or a source to find local data).

Acceleration along the x-axis:

Drag equation ÷ mass = ft/sec which is what we need.  Drag alone is a measure of force.

Acceleration along the y-axis:

Same as above, however acceleration along the y-axis is also affected by gravity.

Atmospheric density = ___________________ slugs/ft3

Visit http://www.digitaldutch.com/atmoscalc/ to calculate atmospheric density based on the altitude and temperature of your specific area.

V=Velocity = _________________ ft/sec

Choose an initial velocity for all students to use (around 70fps)

Angle of attack = __________________ degrees

Choose an initial angle of attack (around 80o)

Drag coefficient = ___________________

We experimentally calculated this value to be about 0.31 for a 2-liter soda bottle

S = Cross sectional area = ____________________ ft2

For a standard 2-liter bottle this value is .0985

W = Weight of object = ___________________ lbs

Choose an initial value (around 0.23 lbs)

g = Gravitational constant = __________________ ft/sec2

32 ft/sec2

m = Mass of object = __________________ slugs

Calculate using the formula W ÷ g = m

As the object moves through the air the angle of attack and the velocity will change due to drag and gravity.  This makes it impossible to predict the outcome based solely on the input data.  Instead, changes in angle and velocity must be considered in very small segments of time.

This is an opportunity to discuss the path that the rocket will follow when drag is included in the calculation.  A good way to introduce this is to consider each path the rocket takes if the velocity changes due to drag are taken into account at different time intervals.

1 second intervals:							vs. 0.5 second intervals:

Though we are given an initial velocity, we will need to understand the horizontal and vertical components of that velocity as they relate to the angle of attack ().

This should be a simple trigonometry problem for students and many will come up with the vertical and horizontal components of velocity on their own.

VerticalVelocity = Velocity

HorizontalVelocity = Velocity

The table below describes how to find the first three rows of the table data for the student worksheet.  The first row will be filled in with all the initial conditions however the last two calculations will require the use of the formula from the first page.  For each column you can see the calculation that should take place.  Consider V0 as the initial V and V1 as V from the next timestep and so on.  Also  = 0.2 s throughout the problem as that is our timestep.  It is important to highlight the connection between the acceleration equation, the change in velocity, and the change in position for the system.

| Time | Horizontal Velocity (Vx) | Vertical Velocity (Vy) | Velocity (V) |  | Horizontal Position (x) | Vertical Position (y) |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.0 |  |  | Initial Velocity from first page | should be 80o | 0 | 0 | Formula from first page with data from this row plugged in along with initial conditions. | Formula from first page with data from this row plugged in along with initial conditions. |
| 0.2 | The velocity from the above cell + the acceleration from the previous timestep*.02 to arrive at new velocity. | The velocity from the above cell + the acceleration from the previous timestep * .02 to arrive at new velocity. | Recalculation of V for use in other equations. |  | New position is the position from the above cell + the horizontal velocity*.02 | New position is the position from the above cell + the vertical velocity*.02 | Formula from first page with data from this row plugged in. | Formula from first page with data from this row plugged in. |
| 0.4 |  |  |  |  |  |  | Formula from first page with data from this row plugged in. | Formula from first page with data from this row plugged in. |

Students may notice that certain values from the acceleration formulas do not change from one row to another. Encourage them to find ways to complete the table faster using the constant values as a single term.

What a Drag! Accommodating Assumptions

Monte Carlo Graph

What a Drag! Accommodating Assumptions

Monte Carlo Graph

Simulation Instructions:

- Open WhatADrag_MonteCarlo.xls

- Using an overhead marker, plot the distance downrange and time of flight for the Default Conditions Results from the yellow box with an X. This is the nominal case.

- Generate a new data point

  - Change the input value for Air Pressure

    - Roll two dice and flip a coin

    - Multiply the values on the dice together

    - If the coin is heads enter the value from step ii in the green Air Pressure/% change (+/-) cell

    - If the coin is tails multiply the value from step ii by -1 and enter the new value in the green Air Pressure/% change (+/-) cell

    - Enter the value from the Air Pressure/New Conditions cell into the green Air Pressure/column B cell

  - Change the input value for Volume of Water using the procedure for Air Pressure

  - Change the input value for Angle Measure

    - Roll two dice and flip a coin

    - Add  the values on the dice together

    - If the coin is heads enter the value from step ii in the green Angle Measure/% change (+/-) cell

    - If the coin is tails multiply the value from step ii by -1 and enter the new value in the green Angle Measure/% change (+/-) cell

    - Enter the value from the Air Pressure/New Conditions cell into the green Angle Measure/column B cell

  - Change the input value for Drag Coefficient using the procedure for Air Pressure

  - Plot the new values from the yellow Results box using a dot.

- Repeat step 3 as many times as possible.

What a Drag! Accommodating Assumptions

Proposal Presentation Scoresheet

| Launch | Distance | Time | Acceptable (Y/N) |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |
| 4 |  |  |  |
| 5 |  |  |  |
| Total Acceptable Flights |  |

Launch Results

Company Name:

Representatives:

Presentation Rubric

|  | 0 | 1 | 2 | 3 | 4 | Score |
| --- | --- | --- | --- | --- | --- | --- |
| Monte Carlo Graph | Less than 50 points plotted | 50 - 74 points plotted | 75-99 points plotted | 100 or more points plotted | 100 or more points plotted on the graph with nominal case and actual results clearly marked |  |
| Explanation of Monte Carlo Graph | No explanation given of how Monte Carlo graph was created | Vague explanation of how Monte Carlo graph was created | Clear explanation of how Monte Carlo Graph was created | Clear explanation of how Monte Carlo graph was created, including an example | Detailed explanation of creation of Monte Carlo Graph including simulations, assumptions, and examples |  |
| Clarity of Presentation | Presentation was difficult to follow | Describes two of the following: rocket design, rocket construction, launch conditions, and launch results | Describes three of the following: rocket design, rocket construction, launch conditions, and launch results | Clearly presents 3 of the following: rocket design, rocket construction, launch conditions, and launch results | Rocket design, construction methods, launch conditions, and launch results clearly presented |  |
|  |  |  |  |  | Total |  |

What a Drag! Accommodating Assumptions

Proposal Presentation Reviewer Scoresheet

Reviewer Name:

Presentation Rubric

|  | 0 | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- | --- |
| Monte Carlo Graph | Less than 50 points plotted | 50 - 74 points plotted | 75-99 points plotted | 100 or more points plotted | 100 or more points plotted on the graph with nominal case and actual results clearly marked |
| Explanation of Monte Carlo Graph | No explanation given of how Monte Carlo graph was created | Vague explanation of how Monte Carlo graph was created | Clear explanation of how Monte Carlo Graph was created | Clear explanation of how Monte Carlo graph was created, including an example | Detailed explanation of creation of Monte Carlo Graph including simulations, assumptions, and examples |
| Clarity of Presentation | Presentation was difficult to follow | Describes two of the following: rocket design, rocket construction, launch conditions, and launch results | Describes three of the following: rocket design, rocket construction, launch conditions, and launch results | Clearly presents 3 of the following: rocket design, rocket construction, launch conditions, and launch results | Rocket design, construction methods, launch conditions, and launch results clearly presented |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |

| Company |
| --- |
| Monte Carlo Graph |  |
| Explanation of Monte Carlo Graph |  |
| Clarity of Presentation |  |
| Total |  |